# Part 1 – General

  - SCOPE

- SUPPLIER: Furnish and install Panel Track Systems (Premium Quality)

- RELATED WORK SPECIFIED ELSEWHERE:

  - Section 06100: Rough Carpentry

  - Section 08520: Aluminum Windows

  - REFERENCES

- FLAME-RESISTANT MATERIALS  SHALL PASS OR EXCEED ONE OR MORE OF THE FOLLOWING TESTS:

- National Fire Protection Association (NFPA) 701 (small scale for horizontal applications)

- Department of Transportation Motor Vehicle Safety Standard 302 Flammability of Interior Materials

- California Administrative Code Title 19

- Federal Standard 191 Method 5903 (used by Port Authority of New York and New Jersey for drapery, curtain, and upholstery material)

- Boston Fire Department Test BFD IX-1

- New York State Uniform Fire Prevention and Building Code

  - SUBMITTALS

  - PRODUCT DATA: Manufacturer’s descriptive literature shall be submitted indicating materials, finishes, construction and installation instructions and verifying that product meets requirements specified. Manufacturer’s recommendations for maintenance and cleaning shall be included.

  - DRAWINGS AND DIAGRAMS: Wiring diagrams of any motorized components or units, working and assembly drawings shall be supplied as requested.

  - SAMPLE: Responsible contracting officer or agent shall supply one sample shade of each type specified in this contract for approval. Supplied units shall be furnished complete with all required components, mounting and associated hardware, instructions and warranty.

  - QUALITY ASSURANCE:

- Supplier: Manufacturer, subsidiary or licensed agent shall be approved to supply the products specified, and to honor any claims against product presented in accordance with warranty.

- INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer shall be responsible for an acceptable installation.

- UNIFORMITY: Provide Panel Track Systems (Premium Quality) of only one manufacturer for entire project.

  - DELIVERY, STORAGE AND HANDLING:

- Product shall be delivered to site in manufacturer’s original packaging.

- Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

  - JOB CONDITIONS:

- Prior to shade installation, building shall be enclosed.

- Interior temperature shall be maintained between 60° F. and 90° F. during and after installation; relative humidity shall not exceed 80%. Wet work shall be complete and dry.

  - WARRANTY:

- Lifetime Limited Warranty. Specific product warranties available from manufacturer or its authorized agent.

PART 2 – Products

  - ACCEPTABLE MANUFACTURER

- Hunter Douglas Architectural / 13915 Danielson St., Ste.100/ Poway, CA 92064/ Phone: 800-727-8953 Fax: 800-205-9819/ Website: http://www.HDarchitectural.com/ or architect approved equivalent.

- Product substitutions must be approved by architect minimum of 30 days prior to close of bid.

  - PANEL TRACK SYSTEMS

- PRODUCT: Hunter Douglas Skyline™ FR Gliding Window Panels

- MATERIALS:

1.	FABRICS: Inherently anti-static, flame retardant, fade and stain resistant fabrics providing 0% - 14% openness factors. Fabric weights to range between 11.79 oz/sq.yd. – 14.60 oz/sq.yd. containing fiberglass, PVC, polyester, & vinyl coatings. Finish selected by architect from manufacturer’s available contract colors.

Panel widths available in 11 ½” and 17”.

2.	CHANNEL: Patented anodized aluminum dual channel single track system measuring 2 1/2” X 3/4”.                                             Internally fit with components required for specified performance and designed for smooth, quiet, trouble-free operation.

3.	TRAVERSING: Stretch resistant, non-fraying, and lint-free lock knit polyester cord provides traversing

capabilities for left, right, and split stack draws.

4.	BOTTOM WEIGHT: Powder coated color-coordinated aluminum interlocking bottom weight provides panel   stability and alleviates panel tangling.

- MOUNTING HARDWARE: Manufacturer’s standard L- bracket with clip (outside mounts) and clip only (inside mounts) provide required support. Available in 3 color options Bronze, Plated, and Ivory.

D.	ADDITIONAL AVAILABLE OPTIONS: Valance, Wand Control

  - FABRICATION

- Shade measurements shall be accurate to within + 1/8” or as recommended in writing by manufacturer.

2.04 FABRICS

- FABRIC selection from the following: (0% Openness) Flocke- Blanc, Sahel, Mississippi, Chartreux, Loutre. (5% Openness) Exotic Hues - Patagonian Glacier, Chamorro Coconut, Palmira Teak. Bamboo - Birch. (10% Openness)   New Orleans - Riverboat White, Magnolia, Chicory, Dijon, Vanilla Belle, Wrought Iron. (14% Openness)  SheerWeave 3000 - White, Sand, Chocolate.

2.05 FINISHES

A.     HARDWARE finish selection from the following: Bronze 064, Dusty Green 204, Gold 235, Ivory 320, Lace 661,

Pewter 810, Silver 276, Very Black 048

PART 3 - EXECUTION

  - INSPECTION:

- SUBCONTRACTOR shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

- OTHER INTERACTING TRADES shall receive drawings of shade systems, dimensions, assembly and installation methods from subcontractor upon request.

  - INSTALLATION:

- INSTALLATION shall comply with manufacturer’s specifications, standards and procedures as detailed on contract drawings.

- ADEQUATE CLEARANCE shall be provided to permit unencumbered operation of shade and hardware.

- CLEAN finish installation of dirt and finger marks. Leave work area clean and free of debris.

  - DEMONSTRATION:

- Demonstrate operation method and instruct owner’s personnel in the proper operation and maintenance of the blinds.

  - SCHEDULE:

- EXTERIOR WINDOWS:

- INTERIOR RELIGHTS:

END OF SECTION 12492