# Part 1 – General

  - SCOPE

- SUPPLIER: Furnish and install Commercial Window Shadings (Premium Quality)

- RELATED WORK SPECIFIED ELSEWHERE:

  - Section 06100: Rough Carpentry

  - Section 08520: Aluminum Windows

  - REFERENCES

- FLAME-RESISTANT FABRICS SHALL PASS OR EXCEED ONE OR MORE OF THE FOLLOWING TESTS:

- National Fire Protection Association (NFPA) 701 (small scale for horizontal applications)

- Department of Transportation Motor Vehicle Safety Standard 302 Flammability of Interior Materials

- California Administrative Code Title 19

- Federal Standard 191 Method 5903 (used by Port Authority of New York and New Jersey for drapery, curtain, and upholstery material)

- Boston Fire Department Test BFD IX-1

- New York State Uniform Fire Prevention and Building Code

  - SUBMITTALS

  - PRODUCT DATA: Manufacturer’s descriptive literature shall be submitted indicating materials, finishes, construction and installation instructions and verifying that product meets requirements specified. Manufacturers recommendations for maintenance and cleaning shall be included.

  - DRAWINGS AND DIAGRAMS: Wiring diagrams of any motorized components or units, working and assembly drawings shall be supplied as requested.

  - SAMPLE: Responsible contracting officer or agent shall supply one sample shade of each type specified in this contract for approval. Supplied units shall be furnished complete with all required components, mounting and associated hardware, instructions and warranty.

  - QUALITY ASSURANCE:

- Supplier: Manufacturer, subsidiary or licensed agent shall be approved to supply the products specified, and to honor any claims against product presented in accordance with warranty.

- INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer shall be responsible for an acceptable installation.

- UNIFORMITY: Provide Commercial Window Shadings of only one manufacturer for entire project.

  - DELIVERY, STORAGE AND HANDLING:

- Product shall be delivered to site in manufacturer’s original packaging.

- Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

  - JOB CONDITIONS:

- Prior to shade installation, building shall be enclosed.

- Interior temperature shall be maintained between 60° F. and 90° F. during and after installation; relative humidity shall not exceed 80%. Wet work shall be complete and dry.

  - WARRANTY:

- Lifetime Limited Warranty. Fabrics and cords warranted for two years. Specific product warranties available from manufacturer or its authorized agent.

PART 2 – Products

  - ACCEPTABLE MANUFACTURER

- Hunter Douglas Architectural / 13915 Danielson St., Ste.100/ Poway, CA 92064/ Phone: 800-727-8953 Fax: 800-205-9819/ Website: HDarchitectural.com, or architect approved equivalent.

- Product substitutions must be approved by architect minimum of 30 days prior to close of bid.

  - COMMERCIAL WINDOW SHADINGS

- PRODUCT: Hunter Douglas “Vignette FR Window Shadings”

- MATERIALS:

  - FABRIC: Combination of permanent flame-resistant 100% polyester fabrics on both front and rear. Constructed of looped overlapping 4” fabric folds located on front with neutral white back fabric providing uniform exterior look. Fabric combination transmits filtered light with no view through. Finish selected by architect from manufacturer’s available contract colors.

  - HEAD/BOTTOM RAIL: Standard headrail type measuring 3.8125” x 3.3125” x .040” thick constructed of aluminum alloy 6063 conceals shading when fully raised. Internally fit with components required for specified performance and designed for smooth, quiet, trouble-free operation. Matching fabric-covered tubular-shaped steel bottom rail provides uniform look. Headrail finish to be standard polyester-based paint and to coordinate with fabric. Ends fitted with engineering plastic end caps measuring 3 13/16” X 3.1875” color coordinated with front fabric.

  - LIFTING/ ROTATION MECHANISM: White engineering plastic spring-tempered rotary clutch system raises and lowers shading providing ease of operation when continuous cord loop is activated and holds shadings in place until force is applied. Color coordinated braided polyester 2.4mm diameter cord loop with tensioner to secure cord loop. Located on either side of individual shade unit as per architect’s request.

  - MOUNTING HARDWARE: Manufacturer’s standard white engineering plastic hidden brackets, provide a sleek, unobtrusive appearance.

  - ADDITIONAL AVAILABLE OPTIONS: Coordinating Fabric Covered Headrail, Motorization, Optional Cord Lengths, Hold Down Brackets.

  - FABRICATION

- Blind measurements shall be accurate to within + 1/8” or as recommended in writing by manufacturer.

2.04 FINISHES

- Fabric finish to be duotone with neutral tone facing the exterior and color selection facing the interior. Color selection from the following: Linen Weave FR 141 Birch Bark, 144 Beechnut, 146 Marshland, 148 Honey Maple, & 228 Sierra Redwood. Heather FR 331 Scottish Dew, 332 Highland Mist, 333 Foggy Bluff, 337 Clover Field, 338 English Derby, & 340 Blue Moss.

PART 3 - EXECUTION

  - INSPECTION:

- SUBCONTRACTOR shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

- OTHER INTERACTING TRADES shall receive drawings of shade systems, dimensions, assembly and installation methods from subcontractor upon request.

  - INSTALLATION:

- INSTALLATION shall comply with manufacturer’s specifications, standards and procedures as detailed on contract drawings.

- ADEQUATE CLEARANCE shall be provided to permit unencumbered operation of shade and hardware.

- CLEAN finish installation of dirt and finger marks. Leave work area clean and free of debris.

  - DEMONSTRATION:

- Demonstrate operation method and instruct owner’s personnel in the proper operation and maintenance of the blinds.

  - SCHEDULE:

- EXTERIOR WINDOWS:

- INTERIOR RELIGHTS:

END OF SECTION 12492