# PART 1 – GENERAL

  - SCOPE

- SUPPLIER: Furnish and install 2” Horizontal FR Faux Wood Blinds (Premium Quality)

- RELATED WORK SPECIFIED ELSEWHERE:

  - Section 06100: Rough Carpentry

  - Section 08520: Aluminum Windows

  - REFERENCES

- FLAME-RESISTANT 2” HORIZONTAL FR FAUX WOODS SHALL PASS OR EXCEED ONE OR MORE OF THE FOLLOWING TESTS:

- National Fire Protection Association (NFPA) 701 (small scale for horizontal applications)

- Department of Transportation Motor Vehicle Safety Standard 302 Flammability of Interior Materials

- California Administrative Code Title 19

- Federal Standard 191 Method 5903 (used by Port Authority of New York and New Jersey for drapery, curtain, and upholstery material)

- Boston Fire Department Test BFD IX-1

- New York State Uniform Fire Prevention and Building Code

  - SUBMITTALS

  - PRODUCT DATA: Manufacturer’s descriptive literature shall be submitted indicating materials, finishes, construction and installation instructions and verifying that product meets requirements specified. Manufacturers recommendations for maintenance and cleaning shall be included.

  - DRAWINGS AND DIAGRAMS: Wiring diagrams of any motorized components or units, working and assembly drawings shall be supplied as requested.

  - SAMPLE: Responsible contracting officer or agent shall supply one sample shade of each type specified in this contract for approval. Supplied units shall be furnished complete with all required components, mounting and associated hardware, instructions and warranty.

  - QUALITY ASSURANCE:

- Supplier: Manufacturer, subsidiary or licensed agent shall be approved to supply the products specified, and to honor any claims against product presented in accordance with warranty.

- INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer shall be responsible for an acceptable installation.

- UNIFORMITY: Provide 2” Horizontal FR Faux Wood Blind of only one manufacturer for entire project.

  - DELIVERY, STORAGE AND HANDLING:

- Product shall be delivered to site in manufacturer’s original packaging.

- Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

  - JOB CONDITIONS:

- Prior to shade installation, building shall be enclosed.

- Interior temperature shall be maintained between 60° F. and 90° F. during and after installation; relative humidity shall not exceed 80%. Wet work shall be complete and dry.

  - WARRANTY:

- Lifetime Limited Warranty. Specific product warranties available from manufacturer or its authorized agent.

PART 2 – PRODUCTS

  - ACCEPTABLE MANUFACTURER

- Hunter Douglas Architectural / 13915 Danielson St., Ste.100 / Poway, CA 92064/ Phone: 800-727-8953 Fax: 800-205-9819/ Website: http://www.HDarchitectural.com/, or architect approved equivalent.

- Product substitutions must be approved by architect minimum of 30 days prior to close of bid.

  - 2” HORIZONTAL FAUX WOOD BLINDS

- PRODUCT: Hunter Douglas “First Edition™ 2” Horizontal FR Alternative Wood Blind”

- MATERIALS:

  - SLATS: 2” wide x 0.105” thick durable PVC. Furnish not less than nominal 7.2 slats per foot to ensure tight closure and light control. Finish with manufacturer’s standard colors selected by architect from manufacturer’s available contract colors.

  - SLAT SUPPORT: Braided ladders of 100% polyester yarn color compatible with slats and spacing of ladder no more than 11”.

  - HEADRAIL: U-shaped profile with rolled edges, measuring 1 1/2” x 2 1/4” x .024” constructed of corrosion resistant steel and providing a sleek low profile design. Internally fit with components required for specified performance and designed for smooth, quiet, trouble-free operation. Headrail finish to be standard baked-on polyester and to coordinate with slats. End caps fitted on headrail for a clean product appearance.

  - BOTTOM RAIL: 1.95” wide x 0.64” thick PVC rectangular in shape. Color-coordinated engineered polymer tape buttons secure the ladder and cord. Finish to be manufacturers standard colors or stained finish to match slats.

  - LIFTING MECHANISM: Engineering polymer and galvanized steel housing cordlocks with polymer roller bearing and steel locking pin system, two-ply polyester cord filler in braided polyester jacket lift cords meet or exceed commercial specification 1029.86, and fracture-resistant polymer cord-stop color-coordinated to slat. Located on either side of individual blind unit as per architect’s request.

  - TILTING MECHANISM: Permanently lubricated and fully enclosed standard cord tilt holds and tilts slats at any angle. Optional wand tilt of worm and gear construction incorporated into tilter mechanism. Solid steel, corrosion resistant tilt rod.

  - TILT CONTROL WAND: Rounded 3/8” diameter constructed of quality selected hardwood stained and lacquered or painted to match slats and detachable without tools. Located on either side of individual blind unit as per architect’s request.

  - MOUNTING HARDWARE: Manufacturer’s standard .030” galvanized steel box brackets with baked-on polyester finish to match headrail with additional support brackets for blinds over 48” wide.

  - VALANCE: Crafted PVC based polymer with finish to match slats.

  - ADDITIONAL AVAILABLE OPTIONS: 2 Blinds on 1 Headrail, Hold Down Brackets, Extension Brackets, Cutouts

  - FABRICATION

- Blind measurements shall be accurate to within + 1/8” or as recommended in writing by manufacturer.

2.04 FINISHES

- SLAT finish selection from the following: 744 Marble Tile, 745 Sundrenched Cotton, 746 Canvas Tote, 747 Lemon Verbena, 749 Vintage Linen

- SLAT SUPPORT braided ladders shall be color coordinated with slat. 530 Natural, 830 Almond

PART 3 - EXECUTION

  - INSPECTION:

- SUBCONTRACTOR shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

- OTHER INTERACTING TRADES shall receive drawings of shade systems, dimensions, assembly and installation methods from subcontractor upon request.

  - INSTALLATION:

- INSTALLATION shall comply with manufacturer’s specifications, standards and procedures as detailed on contract drawings.

- ADEQUATE CLEARANCE shall be provided to permit unencumbered operation of shade and hardware.

- CLEAN finish installation of dirt and finger marks. Leave work area clean and free of debris.

  - DEMONSTRATION:

- Demonstrate operation method and instruct owner’s personnel in the proper operation and maintenance of the blinds.

  - SCHEDULE:

- EXTERIOR WINDOWS:

- INTERIOR RELIGHTS:

END OF SECTION 12492