# PART 1 – GENERAL

  - SCOPE

- SUPPLIER: Furnish and install Commercial Honeycomb Shades (Premium Quality)

- RELATED WORK SPECIFIED ELSEWHERE:

  - Section 06100: Rough Carpentry

  - Section 08520: Aluminum Windows

  - REFERENCES

- FLAME-RESISTANT FABRICS SHALL PASS OR EXCEED ONE OR MORE OF THE FOLLOWING TESTS:

- National Fire Protection Association (NFPA) 701 (small scale for horizontal applications)

- Department of Transportation Motor Vehicle Safety Standard 302 Flammability of Interior Materials

- California Administrative Code Title 19

- Federal Standard 191 Method 5903 (used by Port Authority of New York and New Jersey for drapery, curtain, and upholstery material)

- Boston Fire Department Test BFD IX-1

- New York State Uniform Fire Prevention and Building Code

  - SUBMITTALS

  - PRODUCT DATA: Manufacturer’s descriptive literature shall be submitted indicating materials, finishes, construction and installation instructions and verifying that product meets requirements specified. Manufacturers recommendations for maintenance and cleaning shall be included.

  - DRAWINGS AND DIAGRAMS: Wiring diagrams of any motorized components or units, working and assembly drawings shall be supplied as requested.

  - SAMPLE: Responsible contracting officer or agent shall supply one sample shade of each type specified in this contract for approval. Supplied units shall be furnished complete with all required components, mounting and associated hardware, instructions and warranty.

  - QUALITY ASSURANCE:

- Supplier: Manufacturer, subsidiary or licensed agent shall be approved to supply the products specified, and to honor any claims against product presented in accordance with warranty.

- INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer shall be responsible for an acceptable installation.

- UNIFORMITY: Provide Commercial Honeycomb Shades of only one manufacturer for entire project.

  - DELIVERY, STORAGE AND HANDLING:

- Product shall be delivered to site in manufacturer’s original packaging.

- Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

  - JOB CONDITIONS:

- Prior to shade installation, building shall be enclosed.

- Interior temperature shall be maintained between 60° F. and 90° F. during and after installation; relative humidity shall not exceed 80%. Wet work shall be complete and dry.

  - WARRANTY:

- Lifetime Limited Warranty. Fabrics and cords warranted for three years. Specific product warranties available from manufacturer or its authorized agent.

PART 2 – PRODUCTS

  - ACCEPTABLE MANUFACTURER

- Hunter Douglas Architectural / 12975 Brookprinter PL, Suite 210 / Poway, CA 92064 /

Phone: 800-727-8953 Fax: 800-205-9819/ Website: HDarchitectural.com, or architect approved equivalent.

- Product substitutions must be approved by architect minimum of 30 days prior to close of bid.

  - COMMERCIAL HONEYCOMB SHADES

- PRODUCT: Hunter Douglas “Duette® EasyRise™ Commercial 3/4” FR Semi-Opaque Honeycomb Shades”

- MATERIALS:

  - FABRIC: Permanent flame-resistant textured, non-woven polyester formed into translucent 3/4” hexagonal honeycomb cells in stacked tubular construction. Single cell construction; with each cell an independent piece of fabric. Finish selected by architect from manufacturer’s available contract colors.

  - HEAD/SILL RAIL: EasyRise™ type headrail measuring 2” x 1.875” x .050” thick constructed of aluminum alloy 6063. Internally fit with components required for specified performance and designed for smooth, quiet, trouble-free operation. Finish to be a textured matte to coordinate with the shade fabric. Sill rail measuring 1.875” x .460” x .469” thick constructed of aluminum alloy 6063 with standard polyester based finish color coordinated to fabric. Ends fitted with polycarbonate end caps white in color for headrail and coordinated with fabric for sill rail.

  - LIFTING MECHANISM: White engineering plastic rotary clutch mechanism provides ease of operation when continuous cord loop is activated and holds shade in place unless force is applied. Color coordinated braided polyester .11” continuous cord loop provides uniform cord length with polycarbonate cord tensioner for additional safety. White nylon-covered polyester 2.45mm wide x 0.17”mm thick lift tape allows for easy operation of heavy shades. Located on either side of individual shade unit as per architect’s request.

  - MOUNTING HARDWARE: Manufacturer’s standard nylon coated zinc-plated 1040 HR steel universal hidden brackets, provide a sleek, unobtrusive appearance.

  - ADDITIONAL AVAILABLE OPTIONS: Hold Down Brackets, Motorization.

  - FABRICATION

- Blind measurements shall be accurate to within + 1/8” or as recommended in writing by manufacturer.

2.04 FINISHES

- Fabric finish to be duotone with neutral tone facing the exterior and color selection facing the interior. Color selection from the following: D22-951 Daisy White, D22-457 Journal, D22-907 Beach Shells, D22-989 Bisque, D22-682 Platinum, D22-713 Pearl Gray,  D22-733 Patina Gray, D22-687 Toasted Almond, D22-695 Autumn Harvest, D22-686 Truffle, D22-750 Graphite, D22-749 Black Onyx.

PART 3 - EXECUTION

  - INSPECTION:

- SUBCONTRACTOR shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

- OTHER INTERACTING TRADES shall receive drawings of shade systems, dimensions, assembly and installation methods from subcontractor upon request.

  - INSTALLATION:

- INSTALLATION shall comply with manufacturer’s specifications, standards and procedures as detailed on contract drawings.

- ADEQUATE CLEARANCE shall be provided to permit unencumbered operation of shade and hardware.

- CLEAN finish installation of dirt and finger marks. Leave work area clean and free of debris.

  - DEMONSTRATION:

- Demonstrate operation method and instruct owner’s personnel in the proper operation and maintenance of the blinds.

  - SCHEDULE:

- EXTERIOR WINDOWS:

- INTERIOR RELIGHTS:

END OF SECTION 12492