# PART 1 – GENERAL

  - SCOPE

- SUPPLIER: Furnish and install Commercial Window Shadings (Premium Quality)

- RELATED WORK SPECIFIED ELSEWHERE:

  - Section 06100: Rough Carpentry

  - Section 08520: Aluminum Windows

  - REFERENCES

- FLAME-RETARDANT FABRICS SHALL PASS OR EXCEED ONE OR MORE OF THE FOLLOWING TESTS:

- National Fire Protection Association (NFPA) 701 (small scale for horizontal applications)

- Department of Transportation Motor Vehicle Safety Standard 302 Flammability of Interior Materials

- California Administrative Code Title 19

- Federal Standard 191 Method 5903 (used by Port Authority of New York and New Jersey for drapery, curtain, and upholstery material)

- Boston Fire Department Test BFD IX-1

- New York State Uniform Fire Prevention and Building Code

  - SUBMITTALS

  - PRODUCT DATA: Manufacturer’s descriptive literature shall be submitted indicating materials, finishes, construction and installation instructions and verifying that product meets requirements specified. Manufacturers recommendations for maintenance and cleaning shall be included.

  - DRAWINGS AND DIAGRAMS: Wiring diagrams of any motorized components or units, working and assembly drawings shall be supplied as requested.

  - SAMPLE: Responsible contracting officer or agent shall supply one sample shade of each type specified in this contract for approval. Supplied units shall be furnished complete with all required components, mounting and associated hardware, instructions and warranty.

  - QUALITY ASSURANCE:

- Supplier: Manufacturer, subsidiary or licensed agent shall be approved to supply the products specified, and to honor any claims against product presented in accordance with warranty.

- INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer shall be responsible for an acceptable installation.

- UNIFORMITY: Provide Commercial Window Shadings of only one manufacturer for entire project.

  - DELIVERY, STORAGE AND HANDLING:

- Product shall be delivered to site in manufacturer’s original packaging.

- Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

  - JOB CONDITIONS:

- Prior to shade installation, building shall be enclosed.

- Interior temperature shall be maintained between 60° F. and 90° F. during and after installation; relative humidity shall not exceed 80%. Wet work shall be complete and dry.

  - WARRANTY:

- Lifetime Limited Warranty. Fabrics and cords warranted for two years. Specific product warranties available from manufacturer or its authorized agent.

PART 2 – PRODUCTS

  - ACCEPTABLE MANUFACTURER

- Hunter Douglas Architectural / 13915 Danielson St., Ste.100/ Poway, CA 92064/ Phone: 800-727-8953 Fax: 800-205-9819/ Website: HDarchitectural.com, or architect approved equivalent.

- Product substitutions must be approved by architect minimum of 30 days prior to close of bid.

  - COMMERCIAL WOVEN WOOD FR SHADES

- PRODUCT: Hunter Douglas “Woven Wood FR Shades”

- MATERIALS:

  - FABRIC: Flame retardant treated natural fabrics constructed of woods, reeds, bamboo, & grasses with 100% polyester yarns. Constructed of even overlapping folds when raised and hangs flat in fully lowered position. Fabric selections create sheer and semi opaque applications. Finish selected by architect from manufacturer’s available contract colors.

  - HEAD/BOTTOM RAIL: Standard headrail type measuring 1 ½” X ¾” constructed of wood. Mounted with components required for specified performance and designed for smooth, quiet, trouble-free operation. Matching fabric-rolled ¾” X 3/8” wood bottom rail provides uniform look.

  - LIFTING/ ROTATION MECHANISM: Brown engineering plastic/antique finish metal pulleys with gravity feed cord lock raises and lowers shade providing ease of operation when cord is activated and holds shade in place until force is applied. Color coordinated braided polyester 1.8mm diameter cord with color coordinated wood tassel per individual cord. Located on either side of individual shade unit as per architect’s request.

  - MOUNTING HARDWARE: Manufacturer’s standard metal brackets allow for ceiling or wall installation.

  - VALANCE: Standard 6 ½” in height attached to front edge of headrail system provides uniform look to shade. Standard 1 ½” valance returns provide uniformity to side view of shade.

  - ADDITIONAL AVAILABLE OPTIONS: Clutch Operation, Top Down Bottom Up Applications, Motorization, Optional Cord Lengths, Hold Down Brackets, Extension Brackets

  - FABRICATION

- Blind measurements shall be accurate to within + 1/8” or as recommended in writing by manufacturer.

2.04 FINISHES

- Fabric color selection from the following: Tahiti: FR-WWTA445A96F Coconut. Kathay: FR-WWKA448A96F Beijing Pecan. Safari: Jaguar, Giraffe.

PART 3 - EXECUTION

  - INSPECTION:

- SUBCONTRACTOR shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

- OTHER INTERACTING TRADES shall receive drawings of shade systems, dimensions, assembly and installation methods from subcontractor upon request.

  - INSTALLATION:

- INSTALLATION shall comply with manufacturer’s specifications, standards and procedures as detailed on contract drawings.

- ADEQUATE CLEARANCE shall be provided to permit unencumbered operation of shade and hardware.

- CLEAN finish installation of dirt and finger marks. Leave work area clean and free of debris.

  - DEMONSTRATION:

- Demonstrate operation method and instruct owner’s personnel in the proper operation and maintenance of the blinds.

  - SCHEDULE:

- EXTERIOR WINDOWS:

- INTERIOR RELIGHTS:

END OF SECTION 12492